## Slide 1
Subexawatt laser project XCELS
A.Bashinov, E.Efimenko, A.Gonoskov, E.Khazanov, A.Kim,
I.Kostyukov, A.Muravjov, A.Sergeev, A.Shaykin
Institute of Applied Physics, Russian Academy of Sciences
Nizhny Novgorod, Russia
ExHILP, Heidelberg, 2015
IAP RAS

## Slide 2
IAP RAS
Toward sub-exawatt laser power
From PEARL
PEARL X
XCELS-Proto
to XCELS
Maximization of field intensity
Field structures and new possibilities for extreme light physics
OUTLINE

## Slide 3
IAP RAS
XCELS
XCELS- EXawatt Center for Extreme Light Studies –
is a new research infrastructure selected by the Russian government
among 6 mega science projects to be constructed by 2020.
XCELS is based on a new laser facility comprising of 12 amplification channels,
each of them providing 400 J, 25 fs pulses, with the total pulse power of
almost 200 PW. A new research institute will be built around this laser facility.
12 channels
15 PW each
400 J, 25 fs, 910 nm
Quality: 3 divergence limits
Intensity 1024-1025 W/cm2

## Slide 4
IAP RAS
XCELS versus ELI
Courtesy of W. Sandner
XCELS satisfies requirements for 4th Pillar of ELI
Extreme Light Infrastructure

## Slide 5
IAP RAS
PEARL – PEtawatt pARametric Laser
was launched at IAP in 2006
3 cascades of parametric amplification in DKDP crystals (the final stage
with aperture D=10 cm) provides 1011 total amplification gain

## Slide 6
IAP RAS
Optical Parametric Chirped Pulse Amplification (OPCPA)
Nanosecond pump pulse
Chirped femtosecond signal

## Slide 7
IAP RAS
Superbroadband synchronism e = o+o in DKDP crystal
3 ,k3 – narrow band pump (ns pulse) – frequency 3 = const
1 ,k1 and 2 ,k2 – broadband signal and idler – variables, 1
Рис 1
20
k
r
2
k
r
3
k
r
10
k
r
13
j
(
)
W
j
12
(
)
W
y
12
1
v
r
2
v
r
12
j
Z

## Slide 8
IAP RAS
Superbroadband synchronism e = o+o in DKDP crystal
3 ,k3 – narrow band pump (ns pulse) – frequency 3 = const
1 ,k1 and 2 ,k2 – broadband signal and idler – variables, 1
Рис 1
20
k
r
2
k
r
3
k
r
10
k
r
13
j
(
)
W
j
12
(
)
W
y
12
1
v
r
2
v
r
12
j
Z
=0
phase-matching

## Slide 9
IAP RAS
Superbroadband synchronism e = o+o in DKDP crystal
3 ,k3 – narrow band pump (ns pulse) – frequency 3 = const
1 ,k1 and 2 ,k2 – broadband signal and idler – variables, 1
Рис 1
20
k
r
2
k
r
3
k
r
10
k
r
13
j
(
)
W
j
12
(
)
W
y
12
1
v
r
2
v
r
12
j
Z
=0
phase-matching
=0 broadband phase-matching

## Slide 10
IAP RAS
Superbroadband synchronism e = o+o in DKDP crystal
3 ,k3 – narrow band pump (ns pulse) – frequency 3 = const
1 ,k1 and 2 ,k2 – broadband signal and idler – variables, 1
Рис 1
20
k
r
2
k
r
3
k
r
10
k
r
13
j
(
)
W
j
12
(
)
W
y
12
1
v
r
2
v
r
12
j
Z
At pumping with second harmonic of Nd:glass laser (3 = 527 nm) in DKDP crystal with 85% deuterization, superbroadband synchronism takes place for :
1 = 910 nm, 2 = 1250 nm,  3=37,50 , 13 = 0.70
1/527=1/910+1/1250
=0
phase-matching
=0 broadband phase-matching
=0 super-broadband phase-matching

## Slide 11
IAP RAS
Cr:Forsterite
fs-laser
l=1250nm
Stretcher
Nd:YLF
amplifier
Compressor
CW Yb:fiber pump 10W
l=1077nm
SHG
2nJ
40fs
1nJ
0.6ns
0.8J
1.5ns
l=527nm
l=910nm
0.5mJ
0.6ns
2J
1.5ns
l=1250nm
l=910nm
50mJ
0.6ns
1mJ
2ns
10mJ
12ns
300J
1.3ns
l=527nm
180J
1.2ns
l=910 nm
38J
0.6 ns
0.1J
1.5ns
l=910 nm
24J
43 fs
Front-end system, 2Hz
Power system
Nd:YLF
laser
l=1054nm
Synchronization
system
Pulse shaper
SHG
OPA II
KD*P
OPA I
KD*P
OPA III
KD*P
Nd:glass
amplifier
The scheme of PEARL

## Slide 12
IAP RAS
PEARL parameters
24J/43fs=0.56PW
Focusable to
1022 W/сm2
Contrast: 108 (0.5ns window)
104 (1ps window)

## Slide 13
IAP RAS
From PEARL to XCELS
PEARL | 0.5 PW | Front-end for XCELS-Proto | 2006
PEARL X | 5 PW | Technological upgrade of PEARL | 2014-2015
XCELS - Proto | 2 x 10 PW | Scaling of PEARL to d30 cm DKDP | 2017
XCELS | 12 x 15 PW | Final | 2020

## Slide 14
IAP RAS
From PEARL to PEARL X
 | PEARL | PEARL X | Growth rate
Pulse duration | 45 fs | 25 fs | 2
Pump laser 2ω (527 micron, 2 ns) | 180 J | 270 J | 2 cascades
Crystal size | 10x10 cm2 | 12.5x12.5 cm2 | 1.5
Efficiency (compressed) | 15% | 25% | 1.6
0.56 PW x 2 x 2 x 1.5 x 1.6 = 5 PW
PEARL X: Increasing OPCPA power of
PEARL facility in 10 times

## Slide 15
IAP RAS
From PEARL to PEARL X
4 cascades of parametric amplification in DKDP crystals (2 final stages
with aperture D=12.5 cm) to provide 1012 total amplification gain
Repetition rate to be increased from 1/30min to 1/(1-3)min

## Slide 16
IAP RAS
Laser complex PEARL-X is under construction
pump energy
OPCPA efficiency
pulse duration
compressor efficiency
OPA V
KD*P
20cm dia
70J
1,5ns
Compressor
1.5ns & 30fs
2
Nd:glass
amplifier
320J
2ns
210J
2ns
150J
30fs
5PW
OPA III
KD*P
10cm dia
2w
Nd:glass
amplifier
320J
2ns
210J
2ns
OPA IV
KD*P
15cm dia
140J
1,5ns
Nd:glass
amplifier
210J
2ns
2w
320J
2ns
210J
1,5ns
3 additional OPCPA stages

## Slide 17
IAP RAS
From PEARL to XCELS
PEARL | 0.5 PW | Front-end for XCELS-Proto | 2006
PEARL X | 5 PW | Technological upgrade of PEARL | 2014-2015
XCELS – Proto | 2 x 10 PW | Scaling of PEARL to d30 cm DKDP | 2017
XCELS | 12 x 15 PW | Final | 2020

## Slide 18
IAP RAS
Available Technologies
Crystals 1-3 with 365×400×50 mm size were grown by the high-rate growth
technique for about 40 days. KDP crystal 4 with 140×140×300 mm size was grown by
a conventional technique for about a year

## Slide 19
IAP RAS
Available Technologies
Schematic diagram of the compressor. Gratings G-2 and G-3 are composite here
For normal operation of the 15 PW compressor diffraction gratings
of appropriate size (500 mm × 800 mm) are required. For the radiation
energy of a pulse arriving at the compressor of 500 J, the energy density
in a 40 cm beam will be a little more than 0.4 J/cm2.

## Slide 20
IAP RAS
Available Technologies
"LUCH" facility with parametric amplifier FEMTA at VNIIEF (Sarov) and record characteristics of parametric amplification of femtosecond pulses

## Slide 21
IAP RAS
PW OPCPA laser complex FEMTA Sarov – N.Novgorod
Cr:Forsterite
fs-laser
Stretcher
OPA I
OPA II
OPA III
OPA IV
Compressor 2
Compressor 1
MO& Pump laser system
SHG
SHG
SHG
Pump booster system
“LUCH”
Synchr. system
2nJ
40fs
1nJ
0.6ns
λ=1250nm
2J
1.5ns
λ=1054nm
0.8J
1.5ns
λ=527nm
0.5mJ
0.6ns
λ=910nm
30mJ
0.6ns
λ=910nm
300J
1.3ns
180J
1.3ns
2kJ
1.5ns
1kJ
1.5ns
38J
0.6ns
24J
43fs
100J
0.6ns
70J
70fs
Front-end system
Final power amplifier
Power pre-amplifier
500TW
1PW

## Slide 22
IAP RAS
XCELS
Main Technological Issues:
Scaling of PEARL to 30 cm aperture DKDP crystal
2-3 kJ Nd:glass pump lasers
12 separate amplifying chains with shared front-end
Adaptive optics to provide beam quality and coherent combining
First prototyping stage - XCELS-Proto -
two channel laser facility to be built at IAP RAS

## Slide 23
IAP RAS
XCELS-Proto
PEARL architecture
FEMTA & UFL-2M
architectures
(Sarov)

## Slide 24
IAP RAS
XCELS Layout

## Slide 25
IAP RAS
How to maximize field intensity at given power ?
Rule of thumb for coherent combining of several beams:
To maximize the electric field at focusing point,
radiation of several combining beams should reproduce
configuration of phase conjugated dipole radiation field
Minimum focusing volume:
Minimum focusing volume:
Converging dipole wave as an exact solution of Maxwell equations:
I. Gonoskov, A. Aiello, S. Heugel, and G. Leuchs, Phys. Rev. A (2012)
x
z

## Slide 26
IAP RAS
Coherent combining to mimic a converging dipole wave
Belt-6
Double-Belt-12
Geometry | Power per channel | Intensity, ×1025W/cm2 | I/I(f=1.2) | Equivalent power (f=1.2)
Single beam (f=1.2) | P0=200 PW | 1.2 | 1 | 200 PW
Double-Belt-12 12× (f=0.96) | P0/12 | 13.4 | 11.2 | 2.2 EW
Dipole-Wave | - | 16.7 | 13.9 | 2.8 EW
A. Gonoskov, A. Bashinov, I. Gonoskov,C. Harvey, A. Ilderton, A. Kim, M. Marklund, G. Mourou,,A. Sergeev, PRL (2014)

## Slide 27
Chart: Double-Belt
| 6 | 8 | 10 | 12 | 14 | 16
double-circle | 1.08 | 1.17 | 1.21 | 1.21 | 1.13 | 1.07
Chart: Belt
| 3 | 4 | 5 | 6
circle | 1.14 | 1.05 | 0.92 | 0.8
1.2×1026 W/cm2
Intensity, 1026 W/cm2
Number of beams
Number of beams
single beam (f = 1)
1.3×1025 W/cm2
Ptotal = 180 PW
Double-Belt-12
Belt-6
Dipole-wave (ideal)
1.5×1026 W/cm2
Belt and Double-Belt approximation of dipole wave
IAP RAS

## Slide 28
IAP RAS
Field Structures
E-dipole
H-dipole
Z
Z

## Slide 29
IAP RAS
Nonlinear regimes of pair plasma generation
Gamma-ray source
Converging E-dipole wave – Evgeny Efimenko (poster)
Giant quasistatic magnetic field generation in
colliding laser pulses – Alexander Muraviov (poster)

## Slide 30
IAP RAS
For XCELS information:
www.xcels.iapras.ru
Thank you for your attention